## Slide 1: 8. RESOURCE MANAGEMENT
When and why resource management and control is necessary.
  What a critical section is.
What mutual exclusion means.
What it means to suspend the scheduler.
How to use a mutex.
How to create and use a gatekeeper task.
  What priority inversion is, and how priority inheritance can reduce (but not remove) its impact.

## Slide 2: 8. RESOURCE MANAGEMENT
8.1 When and why resource management and control is necessary.
Accessing Peripherals
Read, Modify, Write Operations
Non-atomic Access to Variables
Function Reentrancy

## Slide 3: 8. RESOURCE MANAGEMENT
8.2 What a critical section is.
Using taskENTER_CRITICAL() and taskEXIT_CRITICAL(),
Not take any parameters, or return a value
The interrupt priority set by configMAX_SYSCALL_INTERRUPT_PRIORITY
The critical section will be exited only when the nesting depth returns to zero
taskENTER_CRITICAL() and taskEXIT_CRITICAL() do not end in ‘FromISR’, so must not be called from an interrupt service routine so we use taskENTER_CRITICAL_FROM_ISR() and taskEXIT_CRITICAL_FROM_ISR()

## Slide 4: 8. RESOURCE MANAGEMENT
8.3 What mutual exclusion means.
To ensure data consistency is maintained at all times
Ensure that, once a task starts to access a shared resource that is not re-entrant and not thread-safe the same task has exclusive access to the resource until the resource has been returned to a consistent state.
Each resource is accessed only from a single task.

## Slide 5: 8. RESOURCE MANAGEMENT
8.4 What it means to suspend the scheduler.(Locking the Scheduler)
Suspending the scheduler only protects a region of code from access by other tasks, because interrupts remain enabled.
If an interrupt requests a context switch while the scheduler is suspended, then the request is held pending and is performed only when the scheduler is resumed (un-suspended).

## Slide 6: 8. RESOURCE MANAGEMENT
8.5 How to use a mutex.
configUSE_MUTEXES must be set to 1 in FreeRTOSConfig.h for mutexes to be available.
First successfully ‘take’ the token and then when the token holder has finished with the resource, it must ‘give’ the token back.
A semaphore that is used for mutual exclusion must always be returned.
A semaphore that is used for synchronization is normally discarded and not returned.

## Slide 7: 8. RESOURCE MANAGEMENT
8.5 How to use a mutex.
As a mutex is used to ensure each task gets mutually exclusive access to the terminal, even when pre-emption occurs, the strings that are displayed will be correct and in no way corrupted.

## Slide 8: 8. RESOURCE MANAGEMENT
8.6 How to create and use a gatekeeper task.
When a task wants to write a message to standard out, it does not call a print function directly but, instead, sends the message to the gatekeeper.
The gatekeeper task uses a FreeRTOS queue to serialize access to standard out.
The only task permitted to access standard out directly.
When a message arrives, the gatekeeper simply writes the message to standard out, before returning to the Blocked state to wait for the next message

## Slide 9: 8. RESOURCE MANAGEMENT
8.7 What priority inversion is, and how priority inheritance can reduce (but not remove) its impact.
A higher priority task being delayed by a lower priority task in this manner is called ‘priority inversion’.
priority inheritance can reduce its impact by ensuring that the inversion is always time bounded.
Moreover, Priority inheritance is included by Mutexes which semaphores do not have
Priority inheritance works by temporarily raising the priority of the mutex holder to the priority of the highest priority task that is attempting to obtain the same mutex

## Slide 10: 8. RESOURCE MANAGEMENT
8.7 What priority inversion is, and how priority inheritance can reduce (but not remove) its impact.
Moreover, Priority inheritance is included by Mutexes which semaphores do not have
Priority inheritance works by temporarily raising the priority of the mutex holder to the priority of the highest priority task that is attempting to obtain the same mutex

## Slide 11: 9. EVENT GROUPS
Practical uses for event groups.
The advantages and disadvantages of event groups relative to other FreeRTOS features.
How to set bits in an event group.
How to wait in the Blocked state for bits to become set in an event group.
How to use an event group to synchronize a set of tasks.

## Slide 12: 9. EVENT GROUPS
9.1 Practical uses for event groups.
event group can be used to simultaneously simplify a design, and minimize resource usage.
if a socket has been created, but not yet bound to an address, then it can expect to receive a bind event, but would not expect to receive a read event (it cannot read data if it does not have an address).

## Slide 13: 9. EVENT GROUPS
9.2 The advantages and disadvantages of event groups relative to other FreeRTOS features.
Event groups allow a task to wait in the Blocked state for a combination of one of more events to occur.
Event groups unblock all the tasks that were waiting for the same event, or combination of events, when the event occurs.
They can useful for synchronizing multiple tasks,
Event groups also provide the opportunity to reduce the RAM used by an application, as often it is possible to replace many binary semaphores with a single event group.

## Slide 14: 9. EVENT GROUPS
9.3 How to set bits in an event group.
If configUSE_16_BIT_TICKS is 1, then each event group contains 8 usable event bits.
If configUSE_16_BIT_TICKS is 0, then each event group contains 24 usable event bits.
First we need to Set Event Flag which include bits we want to set and ORing the event group’s existing value with the value passed in uxBitsToSet
xEventGroupSetBitsFromISR() is the interrupt safe version of xEventGroupSetBits().

## Slide 15: 9. EVENT GROUPS
9.4 How to wait in the Blocked state for bits to become set in an event group.
We wait by using The xEventGroupWaitBits() API (function allows a task to read the value of an event group, and optionally wait in the Blocked state for one or more event bits in the event group to become set, if the event bits are not already set.)
uxBitsToWaitFor specifies which is a mask to set bits
xWaitForAllBits specifies whether to use a bitwise OR test, or a bitwise AND test if pdFALSE -> state change to wait for its unblock condition when ANY bits of uxBitsToWaitFor become set. If pdTURE -> state change to wait for its unblock condition when ALL bits of uxBitsToWaitFor become set

## Slide 16: 9. EVENT GROUPS
9.4 How to wait in the Blocked state for bits to become set in an event group.
xClearOnExit is set to pdTRUE -> uxBitsToWaitFor cleared 0 before calling task exits xEventGroupWaitBits()
xClearOnExit is set to pdFAIL -> State of event bits in the event group are not Modified in xEventGroupWaitBits() API
If the xTicksToWait parameter expires so state will change to wait for its unblock condition regardless of xWaitForAllBits.

## Slide 17: 9. EVENT GROUPS
9.5 How to use an event group to synchronize a set of tasks.
Each task that must participate in the synchronization is assigned a unique event bit within the event group.
Each task sets its own event bit when it reaches the synchronization point.
Having set its own event bit, each task blocks on the event group to wait for the event bits that represent all the other synchronizing tasks to also become set..

## Slide 18: 9. EVENT GROUPS
9.5 How to use an event group to synchronize a set of tasks.
By using SocketTxTask and SocketRxTask
Use a queue to send the socket to the task that receives data.
The xEventGroupSetBits() and xEventGroupWaitBits() API functions cannot be used in this scenario so in this specified recommended to use The xEventGroupSync() API Function

## Slide 19: 10. Task Notifications
A task’s notification state and notification value.
How and when a task notification can be used in place of a communication object, such as a semaphore.
The advantages of using a task notification in place of a communication object.

## Slide 20: 10. Task Notifications
10.1 A task’s notification state and notification value.
When configUSE_TASK_NOTIFICATIONS is set to 1, each task has a ‘Notification State’, which can be either ‘Pending’ or ‘Not-Pending.
When a task receives a notification, its notification state is set to pending.
When a task reads its notification value, its notification state is set to not-pending.
Notification Value is a variable which defined in 32-bit usigned integer.
Task notifications send data to a task by updating the receiving task’s notification value. A task’s notification value can only hold one value at a time.

## Slide 21: 10. Task Notifications
10.2 How and when a task notification can be used in place of a communication object, such as a semaphore.
Because each communication object like ( queue, semaphore or event group) must be created before it can be used.
Limitations of Task Notifications: Task notifications can not be used in: Sending an event or data to an ISR, Enabling more than one receiving task, Buffering multiple data items, Broadcasting to more than one task, Waiting in the blocked state for a send to complete.

## Slide 22: 10. Task Notifications
10.3 The advantages of using a task notification in place of a communication object.
task notification are sent an event or data to a task is significantly faster and requires significantly less RAM than using a queue, semaphore or event group to perform an equivalent operation.

## Slide 23: 11. Developer Support
configASSERT()
FreeRTOS + Trace
Debug Related Hook ( Callback ) Functions
Viewing Run-time and Task State information
Trace Hook Macros

## Slide 24: 11. Developer Support
11.1 configASSERT()
The FreeRTOS source code does not call assert(),
Source code contains lots of calls to a macro called configASSERT(),
configASSERT() improves productivity by immediately trapping and identifying many of the most common sources of error
configASSERT()is not provided -> default empty definition will be used -> all the calls will all removed by C pre-processor.

## Slide 25: 11. Developer Support
11.2 FreeRTOS+Trace
Captures valuable dynamic behavior information
Captured information in interconnected graphical views
FreeRTOS+Trace can be used side-by-side with a traditional debugger

## Slide 26: 11. Developer Support
11.3 Debug Related Hook (Callback) Functions
Malloc failed hook : ensures the application developer is notified immediately if an attempt to create a task, queue, semaphore or event group fails.
Stack overflow hook: ensures the application developer is notified if the amount of stack used by a task exceeds the stack space allocated to the task.

## Slide 27: 11. Developer Support
11.4 Viewing Run-time and Task State Information
Task Run-time Statistics : binary run-time statistics can be call by uxTaskGetSystemState() and ASCII table run-time can be call by vTaskGetRunTimeStats()
configGENERATE_RUN_TIME_STATS = 1 the scheduler will call the others macros
portCONFIGURE_TIMER_FOR_RUN_TIME_STATS choose which peripheral is used to provide the run-time statistic clock

## Slide 28: 11. Developer Support
11.4 Viewing Run-time and Task State Information
portGET_RUN_TIME_COUNTER_VALUE(), or portALT_GET_RUN_TIME_COUNTER_VALUE(Time) : return total time the application has been running since the application first booted.
1st must be defined to evaluate to the current clock value
2nd must be defined to set its ‘Time’ parameter to the current clock value.

## Slide 29: 11. Developer Support
11.4 Viewing Run-time and Task State Information
The uxTaskGetSystemState() API Function : information is provided as an array of TaskStatus_t structures, with one index in the array for each task. Parameter pxTaskStatusArray() must contain at least one TaskStatus_t structure( handle,TaskName, Tasknumber, CurrentState, CurrentPriority, BasePriority, RunTimeCounter, StackHighWatermark)
vTaskList(): similar uxTaskGetSystemState() but presents the infor as ASCII table instead of binary values.

## Slide 30: 11. Developer Support
11.4 Viewing Run-time and Task State Information
vTaskList(pcWriteBuffer) is available if configUSE_TRACE_FACILITY and configUSE_STATS_FORMATTING_FUNCTIONS are both set to 1 in FreeRTOSConfig.h.

## Slide 31: 11. Developer Support
11.5 Trace Hook Macros
Insert code into FreeRTOS without modifying the FreeRTOS source files.
appear in enough places in the FreeRTOS source code to allow them to be used to create a full and detailed scheduler activity trace and profiling log.
traceTASK_INCREMENT_TICK(xTickCount) : The xTickCount parameter passes the new tick count value into the macro.
traceTASK_SWITCHED_OUT(): leave the Running state.
traceTASK_SWITCHED_IN() : enter the Running state

## Slide 32: 11. Developer Support
11.5 Trace Hook Macros
traceBLOCKING_ON_QUEUE_RECEIVE(pxQueue): pxQueue parameter passes the handle of the target queue or semaphore into the macro
traceBLOCKING_ON_QUEUE_SEND(pxQueue) : pxQueue parameter passes the handle of the target queue into the macro.
etc.
FreeRTOS Aware Debugger Plug-ins: eclipse, IAR, ARM DS-5, Atollic TrueStudio, Microchip MPLAB, iSYSTEM WinIDEA

## Slide 33: 12. Trouble shooting
Interrupt Priorities
Stack Overflow
Inappropriate Use of printf() and sprintf()
Other Common Sources of Error

## Slide 34: 12. Trouble shooting
12.1 Interrupt Priorities
the priority of an interrupt that uses the FreeRTOS API cannot be left uninitialized.
Numerically high priority numbers represent logically low interrupt priorities, which may seem counterintuitive, and therefore cause confusion
configMAX_SYSCALL_INTERRUPT_PRIORITY which is assigned a priority numerically higher than this would be valid.
Some libraries will perform the bit shift themselves, whereas others expect the bit shift to be performed before the priority is passed into the library function.

## Slide 35: 12. Trouble shooting
12.1 Interrupt Priorities
Different implementations of the same architecture implement a different number of interrupt priority bits
In some FreeRTOS ports, configMAX_SYSCALL_INTERRUPT_PRIORITY has the alternative name configMAX_API_CALL_INTERRUPT_PRIORITY.

## Slide 36: 12. Trouble shooting
12.2 Stack Overflow
uxTaskGetStackHighWaterMark(): used to query how close a task has come to overflowing the stack space allocated to it
Run Time Stack Checking—Overview:
1. configCHECK_FOR_STACK_OVERFLOW is set to 1: the kernel checks that the stack pointer remains within the valid stack space after the context has been saved
2. configCHECK_FOR_STACK_OVERFLOW is set to 2: tests the last valid 20 bytes, stack overflow hook function is called if any of the 20 bytes have changed from their expected values.

## Slide 37: 12. Trouble shooting
12.3 Inappropriate Use of printf() and sprintf()
Just including a call to printf() or sprintf() can massively increase the size of the application’s executable.
printf() and sprintf() may call malloc(), which might be invalid if a memory allocation scheme other than heap_3 is in use.
printf() and sprintf() may require a stack that is many times bigger than would otherwise be required.
Copies that do not implement snprintf() simply ignore the buffer size parameter, as they map directly to sprintf().

## Slide 38: 12. Trouble shooting
12.4 Other Common Sources of Error
Adding a simple task to a demo causes the demo to crash
Using an API function within an interrupt causes the application to crash
Sometimes the application crashes within an interrupt service routine
The scheduler crashes when attempting to start the first task

## Slide 39: 12. Trouble shooting
12.4 Other Common Sources of Error
Interrupts are unexpectedly left disabled, or critical sections do not nest correctly
The application crashes even before the scheduler is started
Calling API functions while the scheduler is suspended, or from inside a critical section, causes the application to crash